## Slide 1: Workload Characterization of Interactive Cloud Services on Big and Small Server Platforms
Shuang Chen*, Shay Galon**, Christina Delimitrou*,
Srilatha Manne**, and José Martínez*
*Cornell University
**Cavium Inc.

## Slide 2: Executive Summary
How to achieve low tail latency for interactive cloud services?
  Tail latency more important and challenging
  The entire stack from SW to HW is involved
Understand how tail latency reacts to application and system changes
  Quantify how current designs work
  Get insights on future designs
Introduction • Characterization• Implications

## Slide 3: Motivation
Introduction • Characterization• Implications
Notes: Popular interactive cloud services: online translation tool, websearch, real-time navigation tool
A typical 3-tier cloud service: web server, caching, back-end database
- To guarantee low latency of the entire service, each tier is very latency critical
Emerging microservices are composed of even more tiers
- more applications are switching to low-latency ones

## Slide 4: Low Latency
Tail latency
  e.g., QoS defined as 99th %ile in 1ms
0.995 = 0.95
Introduction • Characterization• Implications
0.99
0.99
0.99
0.99
0.99
Notes: For cloud services, it’s not just average latency, but worst-case latency that matters
Quality of service is defined by tail latency.
It is important because
- For developers, it means an overall controllable latency in a high-fanout or multi-tiered framework.
- For users, it means higher probability to get response in an acceptable time, i.e., better user experiences

## Slide 5: Low Tail Latency Requirements
The entire stack from SW to HW is involved
Application
OS
Hardware
Resource Manager
Virtualization
  Application bottleneck
  Different user cases
  Scalability
  Overhead of virtualization
  SW isolation mechanisms
  Overhead of context switching
  HW isolation mechanisms
  Hyperthreading
Introduction • Characterization• Implications
Notes: Application
1. Developers need to identify bottleneck to optimize their codes.
2. They need to understand how their applications are used to optimize for common
3. Applications should scale well with more threads
OS:
1. provide low overhead virtualization techniques
2. Many cloud applications involve a lot of kernel-space processing. There are frequent interrupts, syscalls, and context switching.
3. Provide some isolation mechanisms for resource manager to leverage, e.g, core, memory capacity, network bandwidth partitioning.
Hardware:
Understand and make best use of advanced hardware features
- hardware isolation mechanisms. e.g, LLC capacity and memory bandwidth partitioning
- Hyperthreading, turbo-boost, RAPL, per-core DVFS

## Slide 6: Categorize LC applications
By QoS Strictness
  us: memcached
  ms: web server, in-memory database
  s: persistent database
By Statefulness
  Stateful: memcached
  Stateless: web server
Introduction • Characterization• Implications
Notes: How does stateful and stateless change results?
- In this work, statefulness doesn’t really come into play. But the amount of states will influence LLC and memory capacity and bandwidth requirement. We have a follow-up work that specifically studies resource interference to LC applications, and we see a big difference in LLC and memory bandwidth interference.

## Slide 7: Selected LC Workloads
NGINX
  Web server
  Stateless
  99th% in tens of ms
Memcached
  Key-value store
  Stateful
  99th% in hundreds of us
QoS
Strictness
Statefulness
NGINX
Memcached
Introduction • Characterization• Implications
Notes: Memcached and NGINX are in opposite quadrants, so they are really different and are kind of representative

## Slide 8: Server Architecture
P
L1 I/D: 32/32KB
P
L1 I/D: 32/32KB
LLC: 55MB, 20 ways
Memory: 128G DDR4
…
…22 Cores…
2 Threads/Core
P
L1 I/D: 78/32KB
P
L1 I/D: 78/32KB
LLC: 16MB, 16 ways
Memory: 128G DDR4
…48 Cores…
1 Thread/Core
…
L2: 256KB
L2: 256KB
Intel Xeon E5-2699 v4
Cavium ThunderX
$4,115
$785
NIC: 10Gbps
NIC: 10Gbps
14nm
28nm
Introduction • Characterization• Implications
2.2GHz
1.8GHz
Notes: Differences: cores, #cores, hyperthreading, cache hierachy, process, price. The differences in chip can lead to different single-core or full-socket performance. Price difference is important to reason about TCO in datacenters
The goal is not to provide strict apple-to-apple comparison between these two servers, but give us more insights on how the difference in server architectures come into play when we observe different behaviors in later experiments.

## Slide 9: Studied Parameters
Application
OS
Hardware
Resource Manager
Virtualization
  Application bottleneck
  Different user cases
  Scalability
  Overhead of virtualization
  SW isolation mechanisms
  Overhead of context switching
  HW isolation mechanisms
  Hyperthreading
Introduction • Characterization• Implications

## Slide 10: Input Load
Memcached
NGINX
Xeon
ThunderX
Introduction • Characterization• Implications
5.2x
5x
Notes: Latencies are almost flat at the beginning, but after some threshold, they increase exponentially (y-axis is in log scale)
- compare the dotted and the solid line: tail is about one order of magnitude higher
- compare Xeon and ThunderX: curves look similar, but maximum request-per-second are different (5X higher on Xeon, the Max RPS in the figure is respective maximum request-per-second on each platform)
- investigate what causes the latency increase at high throughput

## Slide 11: Memcached Latency Decomposition
IRQ
Kernel
Syscall
User
Receive
Send
NIC
TCP/IP
Epoll_wait
Read
Libevent
Write
TX
NIC
RX
Request
Response
TCPIP
Memcache
3
1
1
1
5
1
5
1,290
1,650
3
6
14
782
1,009
4
5
9
7
24
ThunderX
At 10% of max throughput
Xeon
6
7
At 90% of max throughput
Xeon
ThunderX
Queuing delay
Introduction • Characterization• Implications
14
20
24
2x slower than Xeon
Network delay
Little user-space processing

## Slide 12: Studied Parameters
Application
OS
Hardware
Resource Manager
Virtualization
  Application bottleneck
  Different user cases
  Scalability
  Overhead of virtualization
  SW isolation mechanisms
  Overhead of context switching
  HW isolation mechanisms
  Hyperthreading
Introduction • Characterization• Implications

## Slide 13: Memcached Value Size
Xeon
ThunderX
  Memory copy
  Network processing and transmission
  ThunderX is more sensitive
Introduction • Characterization• Implications
Notes: Larger values
- result in more time when transferring data.
- result in larger and/or more network response packets, therefore result in more delay in network processing and transmission
ThunderX is more sensitive

## Slide 14: Number of Memcached Items
Xeon
ThunderX
  Cache capacity
  ThunderX is more sensitive
Introduction • Characterization• Implications
Notes: Each item has some metadata. Larger cache helps latency if all the metadata fits in cache.
- ThunderX is more sensitive

## Slide 15: Studied Parameters
Application
OS
Hardware
Resource Manager
Virtualization
  Application bottleneck
  Different user cases
  Scalability
  Overhead of virtualization
  SW isolation mechanisms
  Overhead of context switching
  HW isolation mechanisms
  Hyperthreading
Introduction • Characterization• Implications

## Slide 16: Scalability
Memcached
NGINX
  Interrupt handling
  Load imbalance
  Lock contention
Introduction • Characterization• Implications
Notes: Number of threads is decide during instance instanciation and threads are statically spawned.
Cannot fully utilized the entire socket
- Throughput stops increasing after 16/22 and 36/48 cores because network interrupts. On both platforms, 8 cores are reserved for handling network interrupts.
- NGINX is able to scale further because throughput of NGINX requests are more complex than Memcached, so its throughput is lower, resulting in less network interrupts.
Cannot scale linearly
- load imbalance. i.e., a new Memcached connections are assigned to Memcached threads in a round-robin way
Different user cases 3: number of threads (because)
- lock contention comes from concurrent requests requesting for the same item

## Slide 17: Studied Parameters
Application
OS
Hardware
Resource Manager
Virtualization
  Application bottleneck
  Different user cases
  Scalability
  Overhead of virtualization
  SW isolation mechanisms
  Overhead of context switching
  HW isolation mechanisms
  Hyperthreading
Introduction • Characterization• Implications

## Slide 18: Context Switching
Memcached on Xeon
Memcached on ThunderX
Introduction • Characterization• Implications
  Statically spawned threads VS dynamically allocated cores
  ThunderX is more sensitive
Notes: Hyperthreading is not enabled in this case
When #cores < #threads, multiple threads share a physical core, and experience significant overhead of context switching
- Such effect is more serious on ThunderX
- if threads could be dynamically spawned, then context switching could be avoided and latency drops

## Slide 19: Studied Parameters
Application
OS
Hardware
Resource Manager
Virtualization
  Application bottleneck
  Different user cases
  Scalability
  Overhead of virtualization
  SW isolation mechanisms
  Overhead of context switching
  HW isolation mechanisms
  Hyperthreading
Introduction • Characterization• Implications

## Slide 20: hyperthreading
Reduce the overhead of context switching
  Allocate two threads on two hyperthreads
Make better use of execution units
  Co-locate different applications
Memcached & Nginx on
the same hyperthreads
Memcached & Nginx on
different hyperthreads
Introduction • Characterization• Implications
Notes: Colocate Memcached and NGINX on different hyperthreads on the same cores
- no context switching
- make better use of execution units
- may have issues with contention in private caches

## Slide 21: Implications of These Studies
Reduce network/queuing delays
Optimize common user cases
Improve elasticity
  Lock alternatives
  Load balance
Reduce the overhead of virtualization
Reduce context switching
Make best use of SW isolation mechanisms
Big VS Small Cores
Make best use of HW features
Application
OS
Hardware
Resource Manager
Virtualization
Introduction • Characterization• Implications
Questions?